## Slide 1: High Level Requirements
PR-1. Clock shall display correct time of day when not performing other functions. (U-1, U-2)
PR-2. When the alarm time is reached and the alarm is set to on, the BUZZER shall ring. (U-3).
PR-3. When the BUZZER rings, buttons SW1 or SW2 shall be used to turn off the BUZZER. Only one of SW1 or SW2 needs to be pressed. (U-4)
PR-4. To set the alarm state to ON, in NORMAL mode, both buttons SW1 and SW2 shall be pressed and held down for more than 5 seconds. (U-5)
  PR-4a. When the alarm is ON (ARMED), the ARMED LED light shall be on. (U-6)
PR-5. To set the alarm state to OFF, in NORMAL mode and the alarm is ARMED, both buttons SW1 and SW2 shall be pressed and held down for more than 5 seconds. (U-5)
  PR-5a. When the alarm is OFF (not ARMED), the ARMED LED light shall be off. (U-6)

## Slide 2: High Level Requirements
PR-6. The user shall be able to set the time using SW1 and SW2. (U-1)
  PR-6a. Pressing SW1 and holding it for more than 5 seconds shall advance the time at one hour of time per second that the button is held down. (U-1)
  PR-6b. Pressing SW2 and holding it for more than 5 seconds shall advance the time at one minute of time per second. Holding it for more than 10 seconds will advance the time by 10 minutes of time per second. (U-1)
PR-7. The user shall be able to set the alarm time using SW1 and SW2. (U-7)
  PR-7a. Pressing SW1 when in normal mode shall transition the system into set alarm mode. The user shall see the alarm time in this mode. (U-8)
  PR-7b. Pressing SW2 when in alarm mode shall advance alarm time at one minute of alarm time per second that the button is held down
  PR-7c. Pressing SW2 and holding it for more than 5 seconds shall advance alarm time at 1 hour of alarm time per second that the button is held down. Rationale: speeds up large changes in alarm time.